## Slide 1
Microprocessors Tutorial 1:
Arduino Basics

## Slide 2
6 Analog Pins
14 Digital Pins (6 PWM)
USB
Reset button
Power
Arduino Hardware
Powering the board

## Slide 3
    Lets go through it
Arduino IDE

## Slide 4
Void setup()
  Runs once
Void loop()
  Runs forever!

## Slide 5: Lets Start:
Connect Arduino
  Driver found?
  Correct port? Tools  Port
  Correct Board? Tools -> Board -> “Arduino/Genuino Uno”
Upload the blink Sketch
  Does the light blink?
  File  Examples  Basic  blink
  Press Upload

## Slide 6: Arduino syntax:
pinMode(pin,MODE);
  OUTPUT, INPUT
delay(ms)
digitalWrite(pin,state);
  Writes an int (0 or 1) to a pin
digitalRead(pin);
Returns an int (0 or 1)
Servo.attach(pin)
  Digital Pin 1-13
Servo.write(degree)
  -180 to 180 degree with stall at 90 degrees

## Slide 7: Breadboard:

## Slide 9: IF statements:
if a condition is true  then do something
if( a condition ){
  //do something
}else{
//do something else
}
if( 4>1){
digitalWrite(pin0,HIGH);
}

## Slide 10: Pseudo code
Declare four variable outside setup() to keep track of converted value to send to servo;
Attach the servo to digital pins using servo()
Create an temporary integer to store the analog value you are reading using AnalogRead(Pin);
Map the value from temporary integer
from 0-1023 and -180 to 180 to a fixed variable
5. Write the fixed variable to our servo

## Slide 11: Analog
to pin
+5v
Analog: 0-1023
Potentiometer, sensor, motors
AnalogRead(), analogWrite()
Potentiometer: variable resistance

## Slide 12: Examples:
Servo servo1;
Int result = 0;
Void setup()
{
servo1.attach(pin_number);
}
Void loop()
{
int temp1 = analogRead(pin_number);
result = map(temp1, 0, 1023, min_angle_range, max_angle_range);
servo1.write(result);
}

## Slide 13: Useful Links
ieee.concordia.ca
robowars.ca
Questions? Comments? Suggestions?
Arduino Examples
http://arduino.cc/en/Tutorial/HomePage
https://www.arduino.cc/reference/en/ https://www.arduino.cc/en/tutorial/ping
https://www.arduino.cc/en/Tutorial/Sweep